GROUNDWORKER - GENERIC

| Completed by: R Dobbs |  |
| --- | --- |
| Position: Director |  |
| Date: 22 Dec 2015 |  |
| Review: Annually |  |

GENERIC ‘HAZARD’ CONTROL MEASURES =  All operators trained and competent (NPTC CS30-50 as appropriate).Manufacturer’s instruction manual available. All guards, safety features and warnings in place.  Regular machine maintenance and servicing.

INDG – HSE INDG317 “Chainsaws at work”: AFAG Safety Guides 301-308 HSE INDG 362 “Noise at Work”. HSE INDG 363 “Protect your hearing or lose it”  HS (G) 88 “Guide to Hand Arm Vibration”: INDG317 “Chainsaws at work”; HSE 246/31 “Reducing Risks of HAV Injury From Hand Held Power Tools”;

| Ref: | Hazard | Risk | Persons at risk | Risk level | Control measures | Residual Risk | Further Action Required? | By (date) | Done (date) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| a | Fuelling, (petrol two stroke oil) | 1.Fire/explosion: burns/blast injuries. 2. Skin contact: irritation / dermatitis | Work team/ client/general public | Prob. – M Sev. - VH = HIGH | No smoking. Shaded fuelling site. Safe distance from any ignition source. Correct sealed containers. Saw fuel caps replaced securely. PPE - gloves | Prob. – L Sev. – H = MOD. | Periodic staff meeting reviews and on site auditing for compliance. |  |  |
| b | Maintenance: chain / bar | Cuts from chain / bar / hand tools | Work team | Prob. – M Sev. – L = MOD.-LOW | Avoid bare hand contact with chain and bar. Use of appropriate tools. Ensure files have handles. PPE - gloves | Prob. – L Sev. – VL = LOW | None |  |  |
| c | Noise (typically upto 105dcb) | Noise Induced Hearing Loss / Deafness (accumulative over time) | Saw operator/ work team | Prob. – VH Sev. – VH = V.HIGH | Purchase lowest decibel saws. Correct saw maintenance (exhaust baffles, chain and bar). PPE - Suitable hearing protectors. | Prob. – VL Sev. – M = LOW | Periodic staff meeting reviews and on site auditing for compliance. Annual health surveillance. |  |  |
| d | Vibration | Hand Arm Vibration Syndrome (HAVS) and Vibration White | Saw operator and partic. operators of large & older chainsaws | Prob. – H Sev. – H = HIGH | Purchase lowest vibration saws. Select appropriate equipment, monitor and carefully regulate exposure times against published data. | Prob. – L Sev. – M = MOD.- LOW | Periodic staff meeting reviews and on site auditing for compliance. |  |  |
| Ref: | Hazard | Risk | Persons at risk | Risk level | Control measures | Residual Risk | Further Action Required? | By (date) | Done (date) |
| d | Vibration …cont’d. | Finger (VWF) Repetitive strain injury (RSI) all accumulative over time | See above | See above | Correct maintenance for A/V systems, chain and bar. PPE - gloves. Use of lorry mounted HIAB to reduce the need to cut large diameter or long lengths of roundwood into manageable pieces | See above | Annual health surveillance (or more frequent as required) |  |  |
| e | Poor handling | Muscular strain/ long-term musculoskeletal injury | Saw operator | Prob. – M Sev. – M = MOD. | Use of ergonomic work systems. Work planning. Fit and well operators. | Prob. – L Sev. – M = MOD.- LOW | Manual Handling training to inc. chainsaw specific use. | Dec. 2010 |  |
| f | Contact with moving chain / ‘kickback’ | Cut injuries / lacerations / severed arteries | Saw operator | Prob. – H Sev. – VH = HIGH | Saw safety features fitted and working. ‘Anti-kickback’ chains used. Correct bar and chain maintenance. Correct body positioning. PPE – chainsaw gloves (as dictated by site specific risk assessment) / work gloves | Prob. – M-L Sev. – H =MOD. | Periodic staff meeting reviews and on site auditing for compliance. |  |  |
| g | Inhalation of exhaust emissions | Nausea / sickness, carbon monoxide poisoning Eye irritation | Saw operator / work team | Prob. – L Sev. – M = LOW | Use of low emission fuels. Correct saw and exhaust maintenance / engine tuning. Use only in well ventilated areas. | Prob. – VL Sev. – L = V. LOW | As above |  |  |
| H | Contact with hot exhaust | Burns to skin / ignites flammable materials & clothing | Saw operator / work team | Prob. – L Sev. – M = MOD. | All operators trained and competent (NPTC CS30). Correct saw maintenance and servicing. Correct use and positioning. Correct carrying / transport techniques. Allow saw to cool before transport. | Prob. – VL Sev. – M = LOW | As above. |  |  |

KEY:

| Ref.: | Reference for individual hazard which corresponds with site specific risk assessment form |
| --- | --- |
| Hazard: | The particular hazard described as ‘how’ it will cause harm |
| Persons at risk: | ‘Who‘, or ‘what’, is at risk of harm / damage |
| Risk level: | Risk level prior to implementing control measures (broadly assessed): Prob. = probability / likelihood (VL – very low, L – low, M – moderate, H – high, VH very high) Sev. = severity / extent of harm (VL – very low, L – low, M – moderate, H – high, VH very high) OUTCOMES: V.HIGH (very high), HIGH, MOD. (moderate), LOW, V.LOW (very low) |
| Control measures: | NB Generic controls, and industry guidance (INDG), detailed at start of generic risk assessment. Specific controls, including brief of PPE requirements, to be implemented to achieve reduced risk to acceptable level. |
| Residual risk: | Risk level remaining after implementation of control measures (broadly assessed): Prob. = probability / likelihood (VL – very low, L – low, M – moderate, H – high, VH very high) Sev. = severity / extent of harm (VL – very low, L – low, M – moderate, H – high, VH very high) OUTCOMES: V.HIGH (very high), HIGH, MOD. (moderate), LOW, V.LOW (very low) |
| Further action Required? | Any further action determined as required either specifically, with accompanying dates, or ongoing / general checking / on site auditing. |
| By (date) | By what date is the described ‘further action required’ to be implemented, i.e. Dec. 2010 |
| Done (date) | Has the further action been ‘done’ / completed, to be initialled by ‘responsible person’. |